## Slide 1: oneM2M – OCF Interworking
Dr. Josef J. Blanz
oneM2M Industry Day, September 14th 2018

## Slide 2: Outline
Scope
  Technologies in IoT Stack
  Where OCF & oneM2M play
OCF & oneM2M characteristics
  Topology & simplified examples
  Commonalities & difference
OCF-oneM2M Interworking overview
  Examples Scenario
  Interworking functions and procedures
  Flow for example scenario
Vision of Interworking

## Slide 3: Technologies in IoT Stack
Access
Service Layer aka Service Platform Middleware Enablement Platform
Protocols
Network
Transport
Physical
Link
Session
Presentation
Application
CoAP RTPS
HTTP
Wired
IP
TLS / TCP
Custom IoT Applications
Applications
Industrial Non-IP
WebSocket
DTLS / UDP
IEEE 802.1TSN
Interworking

## Slide 4: oneM2M Topology
Application Service Node
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
AE: Application Entity
CSE: Common Services Entity

## Slide 5: oneM2M RESTful Style & Access Control
Application Service Node
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
Host Resources = State Information
Identifiers, credentials & access control privileges need to be provisioned AEs discover resources
Access Resources = Consume Service
State: Locked
Door Lock

## Slide 6: oneM2M Example
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
Update Lock Status to “Open”
Door Lock
Actuator
Sensors
Keypad
State: Locked
UPDATE
Checking Authorization
OK!
NOTIFY
Unlock
RESP.
State: Open
RESP.

## Slide 7: OCF Topology
OCF Device
S
C: OCF Client (might have limited server capabilities as well)
S: OCF Server
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
S

## Slide 8: OCF RESTful Style & Access Control
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
S
Identifiers, credentials & access control privileges need to be provisioned via onboarding Clients discover Servers
Host Resources = State
Information
Access Resources = Consume Service

## Slide 9: OCF Example
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
S

## Slide 10: OCF Example
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
S
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
OCF Device
C
S
State: Locked
UPDATE
Update Lock Status to “Open”
OK!
Checking Authorization
Unlock
State: Open
RESP.

## Slide 11: Commonalities & Differences
RESTful approach
Services exposed by CRUD access to resources
Discovery
Notifications
Support of access control
Aligned information models
In Common
Designed for local area networks = proximal IoT (e.g. smart home)
Entity hosting state also represents/controls “things” connected to it
Direct communication (P2P) between clients and servers
Relies on LAN (IP) where peers can reach each other
Discovery via local multicasts
Flat hierarchy
“User”-centric (onboarding)
Security & access control bi-lateral, provisioned with onboarding tool
OCF
Designed for wide area networks = distal IoT (e.g. smart city)
State might be hosted on nodes different from those connected to and controlling “things”
Hierarchical overlay topology
Relies on app registration
Routing across hierarchy
Dealing with “store and forward”
Discovery via local lookup
Data hosting a service by itself (history, time-series)
Management-centric (provisioning)
Security & access control distributed, centralized and/or local provisioning
oneM2M

## Slide 12: Example Scenario
OXF Proximal IoT Network e.g. one building
Mobile Network
Facility Operator: Monitor & control all lights
in building & outside
Emergency Button: All lights of building on!! Also street light next to it
C
C
C
S
S
S
S
Street light right next to building
ASN
AE
CSE
LTE
LTE
ASN
AE
CSE
LTE
ASN
AE
CSE
MN
AE
CSE
IN
AE
CSE
IPE / Bridge

## Slide 13: Example Scenario
C
C
C
S
S
S
S
ASN
AE
CSE
ASN
AE
CSE
ASN
AE
CSE
MN
AE
CSE
IN
AE
CSE
Mirrors resources from OCF to oneM2M and vice versa
Converts CRUD requests in both directions
IPE / Bridge

## Slide 14: Example for IPE / Bridge Stack
IPE Bridge
IPv4/IPv6
IEEE 802.11 MAC
OCF Server
UDP
IP Routing
IEEE 802.11 PHY
OCF Data Models
DTLS
COAP
IPv4/IPv6
IEEE 802.11 MAC
COAP
UDP
IP Routing
IEEE 802.11 PHY
Bridge
IPv4/IPv6
DSL Stack
TCP
IP Routing
DSL PHY
DTLS
TLS
AE & CSE
IPv4/IPv6
DSL Stack
TCP
IP Routing
DSL PHY
TLS
HTTP
aligned
Could also be WLAN/WWAN
Might be BT-LE or other short range
HTTP
oneM2M Data Models
AE & CSE
OCF Client

## Slide 15: Exposure of OCF Services to oneM2M
May or may not be hosted on same node as the IPE(s)
Exposed OCF Services clubbed together. Depending on e.g. accounting, functions etc. Access control impact: IPE gets super-set of privileges, oneM2M consumers of services can get individual privileges.
Which OCF Servers are allowed to be exposed need to be determined e.g. during OCF onboarding process.
IPE: Interworking Proxy Entity
oneM2M resources “mirror” &
provide access to OCF state

## Slide 16: OCF to oneM2M: IPE Responsibilities
Determination of OCF Functions to be exposed to the oneM2M System
Creation / Deletion of corresponding oneM2M Resource(s) representing exposed OCF Functions
Mirroring state changes of exposed OCF Functions in oneM2M Resources
Detection of requests on oneM2M side to execute OCF Functions and invocation thereof

## Slide 17: Exposure of oneM2M Services to OCF
Need to determine which oneM2M services to expose (e.g. pre-configuration).
Which OCF Client are allowed to be consume exposed oneM2M services needs to be configured.
Exposed oneM2M services clubbed together. Depending on e.g. accounting, functions, access privileges etc. IPE gets super-set of privileges, OCF consumers of services can get individual privileges.
OCF Servers “mirror” &
provide access to oneM2M state

## Slide 18: oneM2M to OCF: IPE Responsibilities
Determination of oneM2M services to be exposed to the OCF Proximal IoT Network
Instantiation / removal of OCF Servers representing exposed oneM2M services
Mirroring state changes of oneM2M Resources representing exposed oneM2M services in OCF resources hosted on OCF Servers
Detection of requests on the OCF side to consume exposed oneM2M services and execution thereof

## Slide 19: oneM2M-OCF Interworking Flow
OXF Proximal IoT Network e.g. one building
Mobile Network
Facility Operator: Switch the two illuminated lights off!
C
C
C
S
S
S
S
ASN
AE
CSE
ASN
AE
CSE
ASN
AE
CSE
AE
CSE
IN
AE
CSE
UPDATE
UPDATE
RESP
RESP
UPDATE
RESP
Emergency Button pressed:
All lights of building & next street light on!
UPDATE
RESP
UPDATE
RESP
UPDATE
RESP
UPDATE
RESP
NOTIFY
RESP
RESP
NOTIFY
RESP
RESP
NOTIFY
RESP
UPDATE
RESP
RESP
NOTIFY
NOTIFY
RESP
NOTIFY
RESP
RESP
IPE: Exposing all OCF lights and one oneM2M light Operator AE: Subscribed to all light resources OCF-IPE: Client observing all OCF light resources

## Slide 20: Flows & procedures specified in TS-0024
Specified for OCF-to-oneM2M
as well as for
oneM2M-to-OCF
exposure of services
(latter one still being worked on)

## Slide 21: Status
oneM2M TS-0033 specifies general interworking concept
oneM2M TS-0023 defined models for Home Automation & normative mapping to equivalent OCF Device Types
oneM2M TS-0024 specifies detailed interworking for OCF
  Exposure of oneM2M services to OCF still being worked on
  Completion expected next week during TP37
  Will be part of oneM2M Rel-3 (Q4 18)
Relevant OCF Specs: Core, Security, Bridging, Device Types
OCF completing oneM2M-derived OCF resource definition (Q4 18)
Links: https://openconnectivity.org/specs http://www.onem2m.org/technical/published-drafts

## Slide 22: Implementation in OS-IoT
ATIS – a founding partner of oneM2M – started an Open Source effort in 2017 for a oneM2M ASN/ADN library targeting smaller devices
The project is called OS-IOT (www.os-iot.org)
OS-IoT recently started to implement an OCF-oneM2M IPE
First direction is working (OCF-2-oneM2M)
See separate presentation later today
Participation is very welcome
oneM2M HAIM Representation of OCF Resources
OCF Device Lights
Interworking Proxy Entity (IPE)
oneM2M CSE

## Slide 23: Vision of Interworking
802.15.4
802.15.4
Open Standards  “Interworking Glue”

## Slide 24: Thank You!
Dr. Josef J. Blanz jblanz@qti.qualcomm.com Qualcomm Technologies Inc. Principal Engineer M2M & IoT Standards & Industry Fora
Chairman oneM2M Industry Liaison Committee Vice-Chairman oneM2M Technical Plenary

## Slide 25: Backup Material
Sub text

## Slide 26: Vision: Interworking
802.15.4
802.15.4
802.15.4
802.15.4
Edge Routing
802.15.4
Proximal Network (e.g. Home)
802.15.4
Mobile Network
Private Network (e.g. Industrial)
802.3
802.3
802.3
802.15.4
Proxy
LTE
NB-IoT
Cat-M
Cat-M
Cat-M
Cat-M
Xyz MNO